COMPUTING SUBJECT:	Application dns service

TYPE:	Assignment

IDENTIFICATION:	DNS

COPYRIGHT:	Michael Claudius

LEVEL:	Intermediate

TIME CONSUMPTION:	30 minutes

EXTENT:	50 lines

OBJECTIVE:	dns-commands

PRECONDITIONS:	Computer Networks Ch. 2.5

COMMANDS:	nslookup

IDENTIFICATION: DNS

The Mission

We are going to explore the Domain Name Service protocol nslookup

Useful links for this assignment

http://en.wikipedia.org/wiki/Nslookup

Assignment 1a nslookup commands

Start a dos-prompt. Maybe on the fastnet as the wireless probably is blocked for these requests.

Click Start -> Programs -> Accessories -> Command prompt

Give the command nslookup and use the help command to get an overview of the various commands available:

Assignment 1b IP-addresses nslookup

Try to type

cs.mit.edu

apu.ac.uk

cis.poly.edu

rhs.dk

www.rhs.dk

www.vu.lt

www.marmara.edu.tr

or others.

Try to type some IP-addresses:

10.254.0.22

193.219.80.2

Assignment 1c set commands

Start to change the default setup to a MX request type:

set type=MX

Check

rhs.dk

nordea.dk

or similar in your home country.

then change request type to ANY:

set type=ANY or SOA

and look at the domains again..

State the information of

expire

TTL

retry

For rhs.dk. or google.com or others.

Assignment 2 nslookup service

Try to use www.kloth.net. Or use Google to search for other nslookup machines.

Choose Services and run nslookup or dns-lookup services.

Now investigate rhs.dk again.

What is the authoritative name server for rhs.dk?